Scanning Tunneling Microscopy
Scanning Tunneling Microscopy
Zachary Barnett
Solid State II
Dr. Elbio Dagotto
April 22, 2008

---
Outline
Outline
Progression of Microscopy
Quantum Tunneling
STM Operation
Applications of STM
Comparison of STM with Other Microscope Techniques
Atomic Manipulation Using STM

---
Progression of Microscopy
Progression of Microscopy
17th century: optical microscope
Capable of observing single cells and bacteria
However, the average wavelength of visible light is a few orders of magnitude greater than the diameter of a single atom.
Cannot image a single atom with visible light.

---
Progression of Microscopy
Next step: electron microscope
Utilizes the wave-like properties of the electron.
Uses electrons with wavelengths comparable to the diameter of an atom
Can resolve individual bulk atoms
However, high energy electrons will penetrate into the bulk without providing surface information, and low-energy electrons are often scattered by the sample.
Can resolve bulk electrons, but cannot resolve surface electrons.

---
Progression of Microscopy
1982: Scanning Tunneling Microscope
Utilizes quantum tunneling
The tunneling current between the tip and sample can provide a topographical image of a surface with atomic resolution
A change in tip-sample distance by the diameter of a single atom (2-5 Å) causes the tunneling current to change by up to 3 orders of magnitude.

---
Quantum Tunneling
Quantum Tunneling
When an electron encounters a potential barrier higher than its energy, the electron wavefunction exponentially decays
For sufficiently thin barriers, there is a non-negligible probability of finding the electron on the other side.
http://www.nanoscience.com/education/STM.html

---
Quantum Tunneling
http://www.chembio.uoguelph.ca/educmat/CHM729/STMpage/stmdet.htm
Two conducting electrodes separated by an insulating vacuum gap.
If the gap is small enough, a tunneling current occurs as a voltage difference is applied.

---
STM Operation
STM Operation
Piezodrives Px and Py scan the metal tip over the sample surface
Pz controls tip height above surface. Feedback current can be used to maintain constant relative height.
Phys. Rev. Letters 49 (1982)

---
Constant Current mode
Constant Current mode
Gif images from: http://www.fkp.uni-erlangen.de/methoden/stmtutor/stmpage.html
A feedback loop is applied to Pz in order to maintain
a constant tunneling current by keeping the tip at a
constant height relative to the surface.

---
Constant Height mode
Constant Height mode
Feedback loop is disabled and the tip is scanned over
the sample at a constant height. Varying tunnel current
conveys same information as varying vertical tip height
in constant current mode.

---
Barrier Height mode
Tip is scanned over each measurement site, and
distance between tip and sample is varied while
recording dI/ds.

---
Applications of STM  7x7 reconstruction of Si(111)
Applications of STM
7x7 reconstruction of Si(111)
Unit cell contains 49 atoms
Models were unable to reconcile all of the available experimental data
Using STM in 1982, first surface images were produced as well as a new, more accurate model of the surface configuration.
Phys. Rev. Letters 50 (1983)

---
Applications of STM
7x7 reconstruction of Si(111)
Unit cell contains 49 atoms
Models were unable to reconcile all of the available experimental data
Using STM in 1982, first surface images were produced as well as a new, more accurate model of the surface configuration.
Phys. Rev. Letters 50 (1983)

---
Applications of STM
7x7 reconstruction of Si(111)
Unit cell contains 49 atoms
Models were unable to reconcile all of the available experimental data
Using STM in 1982, first surface images were produced as well as a new, more accurate model of the surface configuration.
Phys. Rev. Letters 50 (1983)

---
Applications of STM  DNA imaging
Applications of STM
DNA imaging
Driscol et. al. (1990)
Image scale is 35 Å x 55 Å
Yellow indicates topographical maxima.
Letters to Nature 346 (1990)

---
Comparison of STM with other microscope techniques
Comparison of STM with other microscope techniques
STM advantages:
Gives 3-D images of surfaces direct in real space and on atomic scale in all three dimensions
Uses only bound particles and no lenses
It is nondestructive
It is a structural and chemical method, applicable to both periodic and nonperiodic surface structures
It can also be operated at ambient pressure and in liquids
Helv. Phys. Acta 55 (1982)

---
Atomic manipulation with STM
Atomic manipulation with STM
Vertical mode
Lateral mode
J. Vac. Sci Technol. 23 (2005)

---
Atomic manipulation with STM
First example of lateral mode manipulation.
D. M. Eigler and E. K. Scheizer in 1990
IBM logo written with Xe atoms on Ni(110) surface.
Each letter is 50 Å from top to bottom.
Nature 344 (1990)

---
Summary
STM offers a unique method of atomic scale imaging of surfaces.
Can obtain both topographical and chemical/electrical information about a surface.
Offers several advantages over other microscopy techniques.
Capable of atomic scale manipulation as well as imaging.

---
References
Gerd Binning and Heinrich Rohrer. Scientific American. 253:50-56 (1985)
Ch. Gerber, G. Binnig, H. Rohrer, and E. Weibel. Surface Studies by Scanning Tunneling Microscopy. Physical Review Letters, 49:57-61 (1982)
Nanoscience Instruments http://www.nanoscience.com/education/STM.html
Tit Wah Hui. http://www.chembio.uoguelph.ca/educmat/CHM729/STMpage/stmdet.htm
G. Binnig and H. Rohrer. Scanning tunneling microscopy. IBM Journal of Research and Development, 30(4) (1986)

---
References continued
http://www.fkp.uni-erlangen.de/methoden/stmtutor/stmpage.html
Ch. Gerber, G. Binnig, H. Rohrer and E. Weibel. 7 x 7 Reconstruction on Si(111) Resolved in Real Space. Physical Review Letters, 50(2):120-123, (1983)
Michael G. Youngquist, Robert J. Driscol, and John D. Baldeschwieler. Atomic scale imaging of DNA using scanning tunnelling microscopy. Letters to Nature, 346:294-296, (1990)
G. Binnig and H. Rohrer. Scanning Tunneling Microscopy. Physica, 127B:37-45, (1984)

---
References continued
G. Binnig and H. Rohrer. Scanning tunneling microscopy. Helvetica Physica Acta, 55:726-735, (1982)
Gerhard Meyer et al. Manipulation of Atoms and Molecules with the Low-Temperature Scanning Tunneling Microscope. Jpn. J. Appl. Phys., 40:4409-4413, (2001)
Saw Wai Hla. STM Single Atom/Molecule Manipulation and Its Application to Nanoscience and Technology. J. Vac. Sci. Technol. B, 23:1351-1360, 2005.